## Technical Bulletin #7

# Energy Recovery Wheel Design – There are HUGE Differences in Wheel Construction

Before specifying and installing an Energy Recovery Ventilator, know the differences in Heat Wheel Construction.

Ask the manufacturer to provide you with a sample of the wheel they are providing.

# Text boxes

October 2002

Phone:	(813) 250-0488

Fax:	(813) 250-0128

Competitors Offering:

- Silica gel on Styrene (Plastic)

- Does not meet smoke and flame spread ratings of 25 and 50

- Not easily cleanable

- Plastic Ribbon design

- No purge section

- Design encourages cross contamination

- Turbulent airflow provides for high air pressure drop

Manufacturer = ERV Systems, Inc.

- Aluminum construction with non migrating desiccant

- Equal latent and sensible recovery capacity

- Surpasses NFPA 90 requirements for flame and smoke spread

- Cleanable with low pressure steam or hot water

- Wheel cassette is removable

- Industrial grade belt drive

- Purge system to minimize carryover of exhaust air and promote cleaning

- Laminar flow design provides for very low air pressure drop

Actual wheel thickness

Would you like to know more?  We are available to give a presentation and to discuss these benefits in further detail.  Contact either Bill Slade or Jeff Ross at (813) 250-0488.